-Overall System Description (with top-down approach)
-System and subsystem level
-Block diagrams
-Flow charts
-3D drawings
 -All control and sata signals with their feedback paths

-Technical Specifications

-Design Modifications (changes since the CDR)
-Design changes
-4 wheel, 4 motor drive system
-Solar panel inside the box
-Chassis changed

-Updated Standards
-IR visibility marker/flags
-width of the green rectangle
-7 segment inside the box

-Compability Analysis of Sub-blocks
-Inter lib communication
-RPI --- Arduino standarts ---- UART
(Signal interfaces must be described clearly)

-Compliance with Requirements
-Design Requirements
-follow robot infront
-normal distance: 20 cm
-normal speed: 12 cm/s
-leave the line on externally received command
-within 15 sec
-maintain lateral distance of 10 cm from convoy
-rejoin the convoy as the last robot

-Physical Dimensions
-fit inside 30 cm diameter cylinder placed vertically

-Design Decisions According to the Requirements(give details)
-all the sensors and diff drive
-distance sensor IR
-IP to get distance and direction
-38 kHz IR receiver
-(cant read?) motors
-solar panel to detect laser
-made custom chassis

-Possible Error Sources
-HSV to minimize color change
-environmental light
-uneven surface
-4 wheels
-noise in sensors
-low pass filters
-combining data from multiple sensors

-Test Procedures and Assesment of Test Results(with encountered problems and proposed solutions)

 TP:
-Image Processing
Objective: 1. Determine Distance,Direction,Orientation
        2.Determine leaving command

1) Color Detection
-different colors
-check the range of green that can be detected
-different lighting conditions

1) Rectangle Detection
-edge detected
-tried different shapes

2) Corner Detection (coordinates)

3a) Accuracy of Dist,Dir,Orient

3b)Field of view

-Distance Sensors
-IR
-Ultrasonic

-Solar Panel
-Robot Speed

-Turning

-Leaving (Response Time)

-Following

-Power Delivery

-Resource Management (may need some addition)
-Updated budget
-Power distribution and management
- Updated Gannt